Glider Pre-Solo Quiz—Open-book

(as required by FAR 61.87)

[references: FARs,  AIM, Glider Flying Handbook, Sectional Chart, Aircraft Flight Manual, current weight and balance]

Pilot’s Name: ________________________________Date: _________

Type Glider: Schleicher ASK-21

Instructor: _________________________________

General Rules and Regs etc.

- What does AIM mean?

- Briefly describe FAR 91.3

- State the right of way rules for aircraft that are:

- a. converging

- b. approaching head on:

- c. overtaking:

- d. landing:

- List the documents that must be carried in a glider during flightt:

- List documents that the pilot must carry in the aircraft during flight.

- Who is responsible for determining the airworthiness of the glider before flight?

- Give the source (phone numbers, websites, etc) of official aviation weather forecasts and winds aloft 	that you use.

- What is the minimum time that a crew member may consume any alcoholic beverage and fly?

- Describe the standard (non-radio) in-flight towing emergency signals for:

- a. Towplane wants the glider to release immediately:

- b. Glider can’t release:

- c. Towplane can’t release:

- d. Towplane signal given to indicate that glider’s dive brakes are open:

- Describe the markings (colors) on the airspeed indicator that indicate:

- a. Never exceed speed (Vne):

- b. Normal operating range:

- c. Maneuvers must be conducted with caution and only in smooth air:

- Name the traffic patterns legs:

- What is the first thing you should do in an in-flight emergency?

- While on tow, you lose sight of the towplane. What should you do?

- Describe how to handle a slack tow rope.

- What is a stall?

- What are the six warning signs of a stall?

- What is the minimum altitude for performing an intentional stall?

- What will extending your airbrakes or spoilers do to your stall speed?

- What happens to the strength of a tow rope with a knot in it?

- What circumstances require you to release the glider immediately from tow?

- You join a glider in a thermal. Which way do you turn?

- You discover you cannot see the airport and you are getting low. Should you:

- a. Fly toward a building cumulus cloud?

- b. Make an off-field precautionary landing?

- c. Use the radio to find help?

- On downwind you encounter very strong lift and gain 400 feet above pattern altitude.  Should you 	work the thermal?

- What is the proper corrective action to take while flying in sink?

- How can you tell if you are on a collision course with other aircraft?

- What is a spiral dive?

- How do you recognize it?

- How do you recover from it?

- What is aerobatic flight?

- If a speed brake or spoiler malfunctions in flight, what is required? (Hint: see NTSB Part 830 in 	the FAR/AIM)

- You cannot make it back to the airport and must land out. What considerations would you use to 	select the best field on which to land?

- Explain the limitations of your Student Pilot Certificate.

- For how long is your solo endorsement in your logbook valid?

- What action should you take if your radio becomes inoperable?

- What is a spin?

- What is the minimum altitude for performing an intentional stall?

- What will extending your airbrakes or spoilers do to your stall speed?

- W13 Area Procedures

- List all classes of airspace from field elevation to 5000 ft MSL around Waynesboro Eagles Nest Airport:

- Give the flight visibility and cloud clearance requirements for the above airspaces:

- What is the standard pattern entry altitude at this airport (MSL)?

- Under what circumstances would you not use a left-handed traffic pattern at this airport?

- Assuming you are being towed under standard atmospheric conditions, what action will you take if 	the towrope breaks or releases:

- a. at 20 ft AGL?

- b. at 150 ft AGL?

- c. at 200 ft AGL?

- d. at 400 ft AGL?

- e. at 600 ft AGL?

- Are there times you would not make a 180 degree turn after a rope break at 250 feet?

- Why or why not?

- According to club policy, who must be on the field and give you authorization to solo a club ship?

- Specific to This Aircraft

- What flight instruments must be in operable condition to fly this glider?

- You are flying solo. Do YOU need ballast, and if so, how much?

- You are 6 miles out. What min altitude do you need to assure a safe return & landing?

- How can you be sure the Hotelier clips are properly installed

- Give the appropriate airspeeds for this glider:

- Stall (Vso)

- Minimum sink

- Best L/D

- Maneuvering (Va)

- Maximum aerotowing (Vt)

- Never exceed (Vne)

- Rough air (Vra)

- Maximum cross wind

- At what airspeed do you fly this glider to gain the most distance?

- At what airspeed do you fly this glider to remain airborne for as long as possible?

- At what speed will this glider stall?

- At what speed would you fly this glider for the maximum distance with a 20-knot headwind?

- What is the normal approach-to-landing speed?

- When would it increase and how much?

- What is the maximum glide ratio of this glider?

- At what speed does the maximum glide ratio occur?

- What is the glide ratio of this glider at an airspeed of 60 ?

- What is the maximum pilot weight for this glider when solo?

- With an 180 pound person in the rear seat, what is the maximum weight of the front seat person?

- With an 180 pound person in the front seat, what is the maximum weight of the rear seat person?

- What is the maximum useful load in this aircraft?

- What are the minimum and maximum allowable breaking strengths of the towrope for this glider?

- How do you use the radio to inform common traffic of your intended landing? Give terminology and 	radio frequency to use at this airport:

- What are the recommended steps to recover from a spin in this glider?

- Have you performed a spin recovery with an instructor?

- Give two reasons the canopies need to be covered with a canopy cover or blanket when the plane is parked in the sunshine.